| Medium | Degree of pollution | After 30 minutes contained in the air in the room when appliance is running on max. power |
| --- | --- | --- |
| Drinking water | Permissible 100 CFU/ml |  |
| Air washer | Permissible 1.000 CFU/m3 |  |
| Air in the room was polluted by 113/ m3 of germs | 113 CFU/m3 |  |
| Water in the DELPHIN was filled up with 200 ml of 3x105 CFU/ml each. | 60.000.000 CFU in water bath | It has been proved that only 63 CFU/ m3 remained in the outgoing air of the DELPHIN. This shows that the outgoing air of the DELPHIN is much cleaner (- 55 %) than the air sucked in from the room, even if the water is extremely polluted. |

The same experiment was also carried out with 260 millions of mould spores 
Aspergillus in the water basin:

| Medium | Degree of pollution | Total of mould fungi Average CFU/m3 |
| --- | --- | --- |
| Air in the room was measured three times before vacuuming. | 20 CFU/m3 35 CFU /m3 15 CFU /m3 | 15- 35CFU/m3 |
| Outgoing air - DELPHIN | 15 CFU/m3 10 CFU /m3 0 CFU /m3 | 0 - 15CFU/m3 |
| Water in the DELPHIN was filled up with 200 ml of 1,3x106 CFU/ml each. | 260.000.000 CFU in water basin | It has been proved that only 0-15 CFU / m3 remained in the outgoing air of the DELPHIN. This shows that the outgoing air of the DELPHIN can actually be low in germs, even if the water is extremely polluted. |